Pre-RHIOT Evaluation Sessions Plans

Session Timeline

| Time | Sessions in order |
| --- | --- |
| Intro 10 min | Interview regarding personal training progress and assignments. |
| Session One 15 min | Personal Safety |
| Session Two 30 min | Vessel Inspections and Pre-departure Briefing |
| Session Three 20 min | Navigation Preparation |
| Session Four 15 min | Seamanship |
| Session Five On water 20 min | Manoeuvring, Un-docking and Docking |
| Session Six On water 5 min | Accelerating and Trim |
| Session Seven On water 15 min | Man-overboard Underway |
| Session Eight On water 10-15 min | Navigation Underway |
| Session Nine On water 40 min | Towing Operations |
| Estimated Time 2.5-3.0 hrs |  |
| Night Session 1 hour | Night Navigation |
| No. | ( - Successfully Demonstrated the Skills M - Marginal Performance of Skill/ Had to be Prompted F - Failure to Perform the Skill Task | 1. | 2. | 3. |
| 1. | Personal Safety |  |  |  |
| a. | Personal Protection Dress for worst conditions, and perform buddy check. Detail how equipment provides protection for: .. Floatation .. Insulation .. Protection .. Mobility .. Visibility Bring kit bag |  |  |  |
| b. | Survival – outline heat loss actions, initial strategies and actions if immersion might be prolonged Scenario: It is at night and you have fallen over the side of the rescue boat and no one noticed that you were gone. The Rescue boat is in the area but has not spotted you. |  |  |  |
| c. | Signals Detail equipment carried to attract attention: VHF Radio, Flares, Cell Phone, Strobe, Whistle Flashlight, Dye marker, Mirror, etc |  |  |  |

| No. | Task |  |  |  |
| --- | --- | --- | --- | --- |
| 2. | Vessel Inspection and Pre Departure |  |  |  |
| a. | Dress for actual and forecast conditions |  |  |  |
| b. | Vessel Inspection Conduct an actual daily inspection of vessel, and report deficiencies 1. Personal Protection Equipment 2. Boat Safety Equipment 3. Distress Equipment 4. Navigation Equipment 5. Navigation Lights and Vessel Lights |  |  |  |
| c. | List five or more of the following items in a pre-departure check: 1. Fuel 2. Radio Communications (Weather & Information on board ) 3. Navigation Lights 4. Searchlights 5. Void Spaces Or Tanks (Doors & Deck) 6. SAR Equipment State And Stowage 7. Major Safety Systems (Self Righting) 8. Electronic Navigation Systems (Powered And Tested) 9. Engine Lines, Fittings And Propellers (Steering Test) 10. Rigging Or Mast Works (Roll Cages) |  |  |  |
| c. | Pre Mission Briefing Read out to one candidate as if they were talking to an RCC Controller. Briefing: 1. I will read this scenario out to you as though a Marine RCC controller was giving you the information. 2. You may ask any questions you like but when the phone is hung up you then must brief your crew on the mission. 3. The spot is 10 nautical miles your response speed is 30knots What is your transit time and what ETA would you give RCC 4. Please instruct your crew in regards to vessel positions and responsibilities We have a report from a concerned person ashore regarding two people on board a 22ft Bayliner Trophy drifting onto the rocks in Nonsuch Bay. The vessel is reported to be 300 ft off of Keiwit Rocks. The description of the vessel is a white hull with a blue stripe and a blue dodger. We have issued a General Marine Broadcast and got no reply. We would like you to go and assist this vessel. |  |  |  |
| d. | Conduct a pre-departure briefing using: Situation Mission Execution Administration Communications |  |  |  |

| No. | Task |  |  |  |
| --- | --- | --- | --- | --- |
| 3. | Navigation Preparation |  |  |  |
| a. | Compare heading from GPS, steering magnetic compass and fluxgate compass and inputs to other navigational equipment |  |  |  |
| b. | Check awareness of Collision Regulations with regards to: 1.Lookout, safe speed, risk of collision, action by stand on vessel and give way vessel 2.Priorities between vessels 3.Navigation in or near restricted visibility 4.Distress signals |  |  |  |
| c. | Activate and properly set up the GPS when alongside, check for errors and signal strength (HDOP) Set up waypoints and simple route |  |  |  |
| d. | Activate and properly set-up the radar, using brilliance , gain and tune, and then sea clutter and rain clutter as needed to provide the best picture Deactivate scanner when close to another vessel |  |  |  |
| e. | Explain the difference between the following radar terms: 1.north up and heads up 2.stabilized and unstabilised 3.relative motion and true motion 4.sea clutter and rain clutter |  |  |  |
| f. | Show familiarity with the chart, and chart positions |  |  |  |

| No. | Task |  |  |  |
| --- | --- | --- | --- | --- |
| 4. | Seamanship |  |  |  |
| a. | Secure rope to pole as if attaching towline using two different methods |  |  |  |
| b. | Show proper method of securing a rope to a cleat |  |  |  |
| c. | Correctly coil and stow lines and keep area tidy |  |  |  |
| d. | Tie the following knots 1. Bowline 2. Reef knot 3. Clove hitch 4. Sheet bend |  |  |  |
| e. | Identify and work safely with lines under stress |  |  |  |
| f. | Correctly tie up a vessel alongside Dipping eyes on cleats Rigging slip lines |  |  |  |

| No. | Task |  |  |  |
| --- | --- | --- | --- | --- |
| 5. | Manoeuvring, Undocking and Docking |  |  |  |
| a. | Review start up procedures for vessel, Neutral, Choke/Primer (untie lines) etc… 1. Attach kill switches 2. Positive request for communication, allocation of duties including reporting of distance and lookout 3. Start engine/s 4. Throttle use |  |  |  |
| b. | What are forecast weather and tidal conditions |  |  |  |
| c. | Safe and proper departure from dock |  |  |  |
| d. | Demonstrate use of engines and helm for turning, both ahead and astern Show understanding of pivot points |  |  |  |
| e. | Demonstrate tight space manoeuvring and turning short round Demonstrate use of outboard engines when turning both ahead and astern |  |  |  |
| f. | Demonstrate use of SAP when approaching a strange dock (rocks, nails, hazards, depths) |  |  |  |
| g. | Do a simple docking and then a more difficult docking manoeuvre |  |  |  |
| h. | Demonstrate knowledge of effects of wind and tide on docking, and their indicators |  |  |  |

| No. | Task |  |  |  |
| --- | --- | --- | --- | --- |
| 6. | Accelerating and Trim |  |  |  |
| a. | Demonstrate proper communication with crew prior to increasing and decreasing speed |  |  |  |
| b. | Accelerate smoothly and set the trim for optimum performance |  |  |  |

| No. | Task |  |  |  |
| --- | --- | --- | --- | --- |
| 7. | Man-overboard Underway |  |  |  |
| a. | Demonstrate proper communication with crew on event of man-overboard and decreasing speed |  |  |  |
| b. | Allocate jobs of keeping sight of the person in the water |  |  |  |
| c. | Demonstrate proper approach and placing engines in neutral |  |  |  |
| d. | Demonstrate proper preparation for recovery |  |  |  |

| No. | Task |  |  |  |
| --- | --- | --- | --- | --- |
| 8. | Navigation Underway |  |  |  |
| a. | Demonstrate effective team communications, including closed loop communication |  |  |  |
| b. | Identify point of land visually, identify on radar, and identify on chart |  |  |  |
| c. | Use radar to determine position and monitor distance off dangers, by proper use of the Electronic Bearing Line and Variable Range marker Measure distance off point of land Establish and bearing by use of the cursor |  |  |  |
| d. | Use radar to properly determine risk of collision of another vessel |  |  |  |
| e. | Keep plotter on appropriate range |  |  |  |
| f. | Keep radar on appropriate range, and long range scan as required |  |  |  |
| g. | Use of depth sounder |  |  |  |
| h. | Assess instrument error |  |  |  |
| i | Familiarity with: Radar and Controls Chart Plotter Lack of familiarity will result in attendance at simulator before course |  |  |  |

| No. | Task |  |  |  |
| --- | --- | --- | --- | --- |
| 9. | Towing Operations |  |  |  |
| a. | Demonstrate effective communication prior and during the towing operation |  |  |  |
| b. | Use of SAP when approach a vessel to be towed |  |  |  |
| c. | Fully assess a towing situation, and interview the vessel to be towed |  |  |  |
|  | Prepare tow line, flaking down the line, leading it as required ready for passing |  |  |  |
| e. | Demonstrate passing the tow, including use of a heaving line Rig the tow line on the bollard so that it can be handled, heaved in or surged the tow line effectively and safely |  |  |  |
| f. | Properly and safely turn up the tow line on the bollard |  |  |  |
| g. | Towing emergencies Discuss the actions to take if: a) Towed vessel starts to sink b) Man-overboard from Tow c) Man-overboard from own vessel |  |  |  |

| No. | Task |  |  |  |
| --- | --- | --- | --- | --- |
| 10. | Night Operations |  |  |  |
| a. | Make proper preparation for night operations |  |  |  |
| b. | Lay off at least four courses, taking into account possible traffic, proximity to dangers above and below the water, and existing conditions of visibility. |  |  |  |
| c. | Correct the courses to compass courses |  |  |  |
| d. | Calculate the running time on the three courses for a speed of at least 27 knots |  |  |  |
| e. | Input the route into the plotter |  |  |  |
| f. | Run two of the courses using dead reckoning and stop watch |  |  |  |
| g. | Run two of the courses using the plotter and radar |  |  |  |
| h. | Make appropriate use of the depth sounder |  |  |  |
| i. | Conduct one docking and undocking |  |  |  |
| j. | Conduct two legs of an expanding square search pattern |  |  |  |

| Pre RHIOT On-the-Water Evaluation Details |
| --- |
| Session Location |  | Date and Time of Exam |  |
| Instructor’s Name |  | Phone Number |  |
| Address |  | Email |  |

Instructor’s Signature

Comments on Candidate 1:

Signature Candidate 1

Comments on Candidate 2:

Signature Candidate 2

Comments on Candidate 3:

Signature Candidate 3

**A copy of this Evaluation in its entirety must be returned to the office in order to fulfill the Pre RHIOT On-the-Water Evaluation component.**

# Text boxes

Candidate Names